## Slide 1
Part C. Recording
IP Surveillance Camera
Application Guide

## Slide 2: Agenda
Recording via web
Recording via IP Surveillance software

## Slide 3
Case 1: Recording via web
Note: Recording function only available on Internet Explorer, you will not be able to use recording function if you use a web browser other than IE, for example Firefox, Safari, Chrome, Opera, etc.

## Slide 4
Login to the web administration page of the camera and click the Record button. It doesn’t matter whether the PC you used is in the LAN or from the internet.

## Slide 5
After you click Record button, it will pops up a window ask you to choose a location to save the record.

## Slide 6
After choosing the storage location, the color of Record button will change to red which means it is in recording procedure. When you want to stop recording, click Record button again.
NOTE: You should keep Internet Explorer open while recording.

## Slide 7
You will find that the folder is named by date and the record is in .AVI format.
Here I just record about 1 min and the scene is of little motion, but the file size is 13.7MB. So if you intend to record for a long time, you need to consider about the capacity of your hard disk.

## Slide 8
Playback
After recording, you can playback the recorded video via WEB.

## Slide 9
After recording, you may want to playback the recorded video.
Go to SETTING->BASIC->Camera->Playback, and click the button of “Open files” and select the recorded video.

## Slide 10
The video will play in the middle of the page. You can use control button to play, pause and stop the video.

## Slide 11
Case 2: Recording via
IP surveillance software
Primarily, there are three method you can use to record by using the surveillance software. They are manual record, record by schedule and record on motion.
Before recording, we assume that you have already installed the surveillance software. The software can be found in the disk, or can be downloaded from Bundled Surveillance Software.

## Slide 12
Connect to the camera
(before record start)

## Slide 13
On PC, run main console and click Config->Setting.

## Slide 14
Select the Camera tab and click Insert to add a new camera. Click OK to finish the configuration.

## Slide 15
Then you will be able to see the video.

## Slide 16
Recording

## Slide 17
Method 1. Manual record
If you use manual record, you should start the recording manually, also, you need to manually stop it when you want to finish the recording.

## Slide 18
On PC, run main console and click Config->Setting.

## Slide 19
Select General tab and change the Storage Location

## Slide 20
Go back to the main window, right click on the video screen and choose Manual Record.

## Slide 21
Then on the upper right corner there will be a red point which means that manual record is working.

## Slide 22
When you want to stop recording, you need to right click on the video screen and click Manual Record again.

## Slide 23
Method 2. Record on schedule
You may find that manual record is inconvenient, so you can try to record on schedule.
You can set up a schedule and then the software will record according to the schedule automatically.
You don’t need to manually start/stop recording any more.

## Slide 24
Go to main window, click Schedule icon to set up the time duration for video recording.

## Slide 27
There are two modes you can choose on schedule configuration panel. One is Day Mode and the other is Week Mode.
Day Mode: Schedule the cameras to turn the recorder on and off at the same time every day according to your setting.
Week Mode: Schedule the cameras for each day of the week differently. In addition, you may assign extra holidays under the Week Mode.
Here we just take Day Mode as an example.

## Slide 28
To adjust the schedule, you can move the cursor to the Time Bar and change the length or move the bar sideway to change the start and end points. Or you can click on the Configure icon or double click on schedule information on the screen (highlighted in blue) to obtain the Encoding Option panel (see next slide) and change the setting as wished.

## Slide 29
In time section, you can also change the recording period (Start time and End Time).
Remember to check Record Audio if you want to save audio.
Choose Always Record if you want to record at all time during the scheduled time.

## Slide 30
Or you can choose Record on Motion to start recording when there are motions detected during scheduled time.
To detect motion, you have to define a detection area. Left-click and drag the mouse to draw a detection area (The area will be green).
You can also adjust the sensitivity and the frame interval.
Method 3. Record on motion

## Slide 31
After configuring schedule, go back to main window, click Start->Start Recording Schedule.

## Slide 32
The red point on the upper right corner means that the software is recording. You can click Start->Stop Recording Schedule to stop recording.

## Slide 33
Playback
After recording, you can playback the recorded video via IP surveillance software.

## Slide 34
After recording, you may want to playback the recorded video. Go to main window and click Playback icon to open Playback system.

## Slide 35
Click Open Record

## Slide 36
On the left of the panel, you can choose a date you want to check. The date in red means that there is record during this day. And you will see red/green lines show on the time table implying available recorded video.

## Slide 37
You can select the video clip you want to review by left-clicking and dragging to highlight the time period.
After that you will be able to see video preview and now you can click OK so that we can play back the record.

## Slide 38
You can use control button to play, pause and stop the video.

## Slide 39
When playing video, click on the Cue In/ Cue Out icon at where you want to set as the starting/ ending point of a saved video clip.

## Slide 40
Then you can click Save Video on the left hand side to save the selected video clip to other format.

## Slide 41
The video clip can be saved into .ASF or .AVI format which can be played on other media player. Check Export Audio so that audio can also be saved.
NOTE: The original file format is .DAT which can’t be recognized by other media player