## Slide 1
Part B. Motion Triggered Alarm
IP Surveillance Camera
Application Guide

## Slide 2: Agenda
Send alarm to your FTP server
Send alarm to your E-mail box

## Slide 3
Case 1: Send alarm to your FTP server
In this case, we’re showing you how to send motion triggered alarm to your FTP server. If motion is detected, the camera will send picture to a specified FTP server.

## Slide 4
Step 1 Set up schedule
(Operation On Local PC)

## Slide 5
After login to the camera, go to SETTING->Advanced->Schedule.
In the Schedule selection list, choose FTP-Alarm and select effective time period of the schedule. Here I make it effective from 00 to 24. Then click Add to make the schedule effective for Monday.

## Slide 6
As we have checked Use the same time schedule everyday, it’s no need to set schedule for the remained days. Then you can click OK to finish the schedule setting.

## Slide 7
Also, you can uncheck Use the same time schedule everyday and set the schedule respectively.

## Slide 8
Step 2 Set up motion detection
(Operation On Local PC)
Please note that you can only set up motion detection function on Internet Explorer.

## Slide 9
Go to SETTING -> Advanced -> Motion detection.
Check Motion detection 1 and adjust the detecting area by using mouse.
You can set up a total of 3 detecting area.
Notes: 图片未更新！
<number>

## Slide 10
Adjust Threshold and Sensitivity value.
Threshold means the extent which the alarm will be triggered. The less the value is, the easier the alarm be triggered.
Sensitivity means that how often the sensor will scan the image. The higher sensitivity it is ，the more frequently it scans.
After that click OK to finish the settings.
Notes: 图片未更新！
<number>

## Slide 11
Step 3 Set up FTP client
(Operation On Local PC)
You should set up a FTP server which can be connected from the LAN which the camera is in. And the port of the FTP server should be 21.

## Slide 12
Go to SETTING->Advanced->FTP client ->General and check On to enable FTP client function.

## Slide 13
In FTP server name field, just type the IP or the domain of your FTP server. Only IP/domain without prefix ftp:// .
The User name and Password are the account to log on to the FTP server.
If you select Passive mode On, it will connect to the FTP server using passive mode. Whether you should choose On or Off depends on the FTP server.
After that, click Test to test the configuration.

## Slide 14
If you can see the message “FTP Test Success”, it indicates that the configuration is right.
Notes: 图片未更新！
<number>

## Slide 15
Go to SETTING->Advanced->FTP client ->Alarm sending and check On to enable Alarm sending.

## Slide 16
In Remote path field, type in the path to the destination on the FTP server.
The Image File name is the file name you want to assign to the images when sending to the FTP server.
If you select Date Time as Suffix, then Date & Time suffix will be added to the image file name.

## Slide 17
Check Motion detection to enable Alarm. If you didn’t configure motion detection before, you can now click Motion detection button to set up motion detection.
Select Effective Period. You can choose Always or Schedule. Here we choose Schedule as an example and thus the alarm sending will be effective during the period which is set in the schedule. If you didn’t configure schedule before, you can now click Schedule button to set up the schedule.

## Slide 18
Step 4 Check the image file on your FTP server

## Slide 19
If there is motion detected by the camera, the camera will capture the image and then send it to the specified FTP server.
You can see the file name is image file name + date & time.
Notes: 图片未更新！
<number>

## Slide 20
Case 2: Send alarm to your E-mail box
In this case, we’re showing you how to send motion triggered alarm to E-mail box. If motion is detected, the camera will send a mail with picture attached to a specified E-mail box.

## Slide 21
Step 1 Set up schedule
(Operation On Local PC)
Please refer to Case 1 Step 1, but in the Schedule selection list, choose e-Mail(SMTP)-Alarm.

## Slide 22
Step 2 Set up motion detection
(Operation On Local PC)
Please refer to Case 1 Step 2

## Slide 23
Step 3 Set up SMTP client
(Operation On Local PC)

## Slide 24
Go to SETTING->Advanced->SMTP->General and check On to enable SMTP function.

## Slide 25
Notes: 图片未更新
<number>

## Slide 26
In SMTP server name and SMTP server port, type in the correct SMTP server and port. If necessary, please check SSL.
The User name and Password are for you to log on to the mail server, make sure they are correct.
And the above settings is depends on your SMTP server.
The Recipient e-Mail address is the E-mail address where you want the alarm mail be sent to.
Administrator e-mail address used for reply mail and sending system messages from the SMTP server.
Subject is the subject/title of the e-Mail.
Message is the text of the E-mail.
After fill in all the fields, click Test to test the settings.

## Slide 27
If you can see the message “SMTP Test Success”, that means the configuration is right.
Notes: 图片未更新
<number>

## Slide 28
Go to SETTING->Advanced->SMTP->Alarm sending and check On to enable Alarm sending.

## Slide 29
Check File attachment On, so that E-mail will be send with picture attached.
The Image File name is the file name you want to assign to the images when sending to the E-mail box.
If you select Date Time as Suffix, then Date & Time suffix will added to the image file name.

## Slide 30
Check Motion detection to enable Alarm. If you didn’t configure motion detection before, you can now click Motion detection button to set up motion detection.
Select Effective Period. You can choose Always or Schedule. Here we choose Schedule as an example and thus the alarm sending will be effective during the period which is set in the schedule. If you didn’t configure schedule before, you can now click Schedule button to set up the schedule.

## Slide 31
Step 3 Go and Check the Email box

## Slide 32
If there is motion detected by the camera, the camera will capture the image and send a mail attached with the image file to the specified E-mail box.
Notes: 图片未更新
<number>